## Slide 1: Over-Approximating Neural Networks for Verification, Robustness, and Explainability
Serge DURAND (CEA). PhD Candidate ED-STIC, Paris-Saclay
Co-supervisor: Zakaria CHIHANI (DILS/LSL)
Co-supervisor: Caterina URBAN (ENS/Inria ANTIQUE)
Director: François TERRIER (DRT/LIST)
PhD Defense, 19/12/2025

## Slide 2: The need for trustworthy AI
The AI Incident Database https://incidentdatabase.ai/
More than 1200 incidents reported!
Notes: First let’s motivate the need for trustworthy AI if anyone still needs convincing:
List of incidents
Exemple includes safety, biases, unethical use, loss of life

## Slide 3: Aspects of Trustworthiness
Robust training
  Enforcing the stable prediction on similar inputs at training time
Verification
Proving the model has the desired behavior
Correct
Error
Explainability
Highlight the reason behind the decision of the model

## Slide 4: Verifying Neural Networks
1

## Slide 5: Global Safety
Reluplex: An Efficient SMT Solver for Verifying Deep Neural Networks [Katz 2017]
Property: If the intruder is directly ahead and is moving towards the ownship, the Clear of Conflict command should not be advised
Notes: Neural network verification is particularly important for safety-critical applications. Here we have an example of a network designed to prevent aircraft collisions. On the right I show a simplified version of the neural network. It is composed of several layers. The inputs are processed by the sequential application of linear functions followed by a non-linear activation function.

## Slide 6: Verification of Neural Networks
Input-output properties
Correct
Error
Notes: This is an example of input output property.
Such properties can be defined by :
An input set, representing possibly infinitely many inputs
A trained network, here with some fixed given parameters theta
And a safe output space, here for instance a half space, defined by the hyperplane in red.
Any outputs above the hyperplane are considered correct outputs, and the other are errors.

## Slide 7: Exact Verification
Safe :)
Correct
Error
Unsafe :(
Correct
Error
NP-Complete [Katz2017]
Reluplex: An Efficient SMT Solver for Verifying Deep Neural Networks [Katz 2017]

## Slide 8: Over-approximating Neural Networks
Layer 1
Layer 2
Layer 3
Layer k
Input space
Exact reachable space and its over-approximation

## Slide 9: Linear Approximations
Notes: Principle : propagating upper and lower bounding linear functions through the network.

## Slide 10: Over-approximations for verification
Unknown
Correct
Error
Correct
Error
Safe!

## Slide 11: Input partitioning
False Alarm ?
Correct
Error
1) Partition the input space
Formal Security Analysis of Neural Networks using Symbolic Intervals [Wang 2018]
2 ) Solve two verification problems
Correct
Error
Correct
Error

## Slide 12: Iterative input partitioning
  X1: [-1,1]
  X2: [-1,1]
X2: [-1,0]
X2: [0,1]
X1: [0,1]
X1: [-1,0]
X2: [0;0.5]
X2: [0.5,1]
Notes: The process can be repeated and subproblems handled in parallel.
Theoretical convergence (asymptotic complete verification) depends on the linear approximation used.
In practice : repetitive splits do lead to shrinking of the output space, but analysis can timeout (property is unsafe with hard counter examples, network has a large number of inputs…)
Prioritizing inputs to be partitioned is key for efficient analysis.

## Slide 13: “Real life” example
Industrial Use Case
3133 subproblems to solve!

## Slide 14: Existing heuristics:
Random
Largest interval
Gradient Smear [ReluVal, Wang 2018]
backward pass to bound input gradients given pre-computed output bounds.
Over-approximation of the outputs (symbolic intervals for ReluVal)
Final score: largest upper bound times input width
Our proposal: reuse information already computed during the over-approximation
Formal Security Analysis of Neural Networks using Symbolic Intervals [Wang 2018]

## Slide 15: ReCIPH: (Relational coefficient for input partitioning heuristic)
ReCIPH score for the input
Variable to split first: highest ReCIPH score
Notes: Average of the magnitude of linear coefficient applied to the input in lower and upper approximations,
Scaled by the width of the input bounds.
Intuition: if we shrink this input interval the result in the output interval will be the highest. Note: sum would work the same…

## Slide 16: Impact on our use case
879 subproblems
3113 subproblems
Notes: From 3 800

## Slide 17: ACAS Xu benchmark
Properties | Width | ReCIPH | Gradient Smear
1 | 68 567 | 15 289 | 16 521
3 | 319 306 | 16 140 | 209 924
4 | 25 906 | 1 828 | 2 206
5 | 142 637 | 7 023 | 29 169
9 | 3 055 | 2 395 | 3 877
10 | 1 331 | 335 | 217
Reported metric: number of subproblems

## Slide 18: Wider applicability
LIBRA (Fairness analysis)
LIBRA https://caterinaurban.github.io/project/libra/
VNN Comp 2024 report, Verifying Neural Networks with PyRAT [Lemesle 2025], The Fifth International Verification of Neural Networks Competition (VNN-COMP 2024): Summary and Results [Brix 2024]
Verification remains a hard challenge!
PyRAT : 6/12 benchmarks in VNN-COMP 2024 where PyRAT finished 2 / 8 tools

## Slide 19: Over-Approximations for Empirical Robustness
2

## Slide 20: Local Robustness
Explaining and Harnessing Adversarial Examples [Goodfellow 2015]
Pandas (57.7% confidence)
Gibbon (99.3% confidence)

## Slide 21: Neural Network Supervised Training
Error of the prediction (estimated with a loss function)

## Slide 22: Neural Network Supervised Training
Updated parameters
After minimizing the error

## Slide 23: Robust Training
On the Effectiveness of Interval Bound Propagation for Training Verifiably Robust Models [Gowal 2018]
Worst case of the over-approximation of the reachable space
Certified Training (CT)

## Slide 24: Robust Training
On the Effectiveness of Interval Bound Propagation for Training Verifiably Robust Models [Gowal 2018]
Certified Training (CT)
Minimizing the worst-case of the approximation: leads to tighter approximation
Updated parameters

## Slide 25: Robust Training
On the Effectiveness of Interval Bound Propagation for Training Verifiably Robust Models [Gowal 2018]
Adversarial Training (AT)
Output computed on an adversarial perturbation

## Slide 26: Robust Training
On the Effectiveness of Interval Bound Propagation for Training Verifiably Robust Models [Gowal 2018]
Adversarial Training (AT)
Minimizing the error on adversarial perturbations: leads to better empirical robustness
Updated parameters

## Slide 27: Combining Certified and Adversarial Training
Expressive Losses for Verified Robustness via Convex Combinations [De Palma 2024]
AT
CT
(CT + AT)

## Slide 28: Trade-offs
Training Method | Standard (%) | Empirical (%) | Verified (%)
Standard | 91.27 | 0 | 0
AT | 77.07 | 40.14 | 0
CT | 48.51 | 35.48 | 34.97
CT + AT | 53.35 | 36.02 | 35.44
CTBench: A Library and Benchmark for Certified Training [Mao 2024]
CIFAR-10, CNN-7, = 8 / 255.

## Slide 29: Cost of adversarial training:
Towards Deep Learning Models Resistant to Adversarial Attacks [Madry 2018]
PGD

## Slide 30: Single Step Training?
Explaining and Harnessing Adversarial Examples [Goodfellow 2015]
FGSM

## Slide 31: Catastrophic Overfitting
Fast is better than free: revisiting adversarial training [Wong 2020]
FGSM
Robust Accuracy against multi-step attacks
Robust Accuracy against single-step attacks
CIFAR10, PreactResnet18,

## Slide 32: Mitigations
Noisy single steps attacks
Fast is better than free: revisiting adversarial training [Wong 2020], Make Some Noise: Reliable and Efficient Single-Step Adversarial Training [De Jorge 2022]
RS-FGSM
N-FGSM

## Slide 33
Over-approximations and catastrophic overfitting
Bounds decrease with stronger attacks
Adding noise is not enough to consistently mitigate catastrophic overfitting?
CIFAR10, PreactResnet18. Mean and 95% CI over 5 runs
Over-approximated output bounds

## Slide 34
Over-approximations and catastrophic overfitting
High verifiability!
?
Our proposal: use over-approximations at training time for empirical robustness

## Slide 35: CT for Empirical Robustness
CIFAR10, PreactResnet18,
CT + FGSM can prevent catastrophic overfitting on FGSM
CIFAR10, PreactResnet18
Also prevent CO and improves robustness for N-FGSM
CT
CT

## Slide 36: CT for Empirical Robustness
Training Method | Empirical (%)
CT + N-FGSM | 14.79
CT + PGD-5 | 16.45
PGD-10 | 15.14
PGD-5 | 11.47
N-FGSM | 0.23
CIFAR10, CNN-7, 30 Epochs
CIFAR10, CNN-7, 160 Epochs
Performance improvement (w.r.t underlying attack):
On longer training schedules
On easier datasets
On shallower networks
CT
Can over-approximations be used beyond robustness?

## Slide 37: Over-approximations for Explainability
3

## Slide 38: Feature Attributions
Right for the wrong reasons, the need for Explainability
Identify inputs contributing to the network’s decision: improve trust, help diagnose bad models …
But what if the method does not highlight truly important inputs?
CAM-Based Methods Can See through Walls [Taimeskhanov 2024]

## Slide 39: Formally Robust Explanations
Abduction-Based Explanations for Machine Learning Models [Ignatiev 2018]
Binary attribution: irrelevant or relevant
Irrelevant pixel: perturbing it (locally) does not change the prediction (= provable robustness!)
Subset-Optimal: if perturbing any new pixel together with the irrelevant features changes the prediction
Key metric: size of the irrelevant feature set (larger = simpler explanation)

## Slide 40: Formally Robust Explanations
Each step: solving a verification problem!
Active area of research to increase scalability
VeriX: Towards Verified Explainability of Deep Neural Networks [Wu 2023]
Candidate
Irrelevant
Relevant

## Slide 41: Over-approximations For Explainability
VeriX: Towards Verified Explainability of Deep Neural Networks [Wu 2023], A dive into formal explainable attributions for image classification [Doncenco 2025]
Use over-approximations for scalability?
Too Many Unknowns!
Irrelevant
Relevant
Unknown

## Slide 42: Lowering the robustness goal
Saliency map
Mask top k %

## Slide 43: Over-approximations For Explainability
Use over-approximations for scalability?
Use robust models?
Everything Irrelevant!
Explanation is empty

## Slide 44: Over-approximations For Explainability
Everything Irrelevant!
Explanation is empty
Unknowns might hide
this possibility!
Use over-approximations for scalability?
Use robust models?

## Slide 45: Training For Explainability
Make sure the entire input is Empirically Formally Explainable (EFX)
  there exist a successful perturbation (empirically estimated)
  there is at least one irrelevant feature (provably assessed with over-approximations)
Use robust training with lowered robustness goal to prevent full irrelevancy
Our propositions:

## Slide 46: Lowering the robustness goal
Saliency map
Mask top k %
Adversarial training: lower the perturbation radius
Expressive Losses: lower the coefficient associated with the IBP loss
Train to be robust on a subset of inputs (Feature Subset Certified Training)

## Slide 47: Results
Perturbation | Training Method | Accuracy (%) ↑ | Avg Irrelevant set ↑ (# features: 4096) | # EFX(AA) ↑ (samples: 1000)
4 / 255 | Standard |  |  | 
 | Adversarial (1 / 255) |  |  | 
 | CT + Adv (0.5 / 255) |  |  | 
 | FS CT + Adv (2 / 255) |  |  | 
8 / 255 | Standard |  |  | 
 | Adversarial (4 / 255) |  |  | 
 | CT + Adv (1 / 255) |  |  | 
 | FS CT + Adv (4 / 255) |  |  | 
TinyImageNet, CNN-7

## Slide 48: Results
Perturbation | Training Method | Accuracy (%) ↑ | Avg Irrelevant set ↑ (# features: 4096) | # EFX(AA) ↑ (samples: 1000)
4 / 255 | Standard | 54.80 | 23 | 990
 | Adversarial (1 / 255) | 52.61 | 340 | 911
 | CT + AT (0.5 / 255) | 44.79 | 804 | 947
 | FS CT + AT (2 / 255) | 48.60 | 506 | 996
8 / 255 | Standard | 54.80 | 6 | 887
 | Adversarial (4 / 255) | 41.41 | 263 | 925
 | CT + AT (1 / 255) | 42.36 | 465 | 988
 | FS CT + AT (4 / 255) | 44.49 | 684 | 998
TinyImageNet, CNN-7
Non-trivial irrelevant features set on TinyImageNet!
Feature Subset training offers better trade offs for large epsilon

## Slide 49: Conclusion
3

## Slide 50: Contributions
ReCIPH: a heuristic to improve verification relying on partitioning and over-approximations (Workshop Poster WFVML 2022)
Using Certified Training for Empirical Robustness (Journal TMLR 2025)
Using Certified Training to scale Formal Explainability (submission in preparation)

## Slide 51: Future Work
Verification:
Automated input partitioning beyond bissection
Verification of more complex architectures
Verification of more complex properties
Formal Explainability:
True end to end learning of which input are relevant jointly with the robust training for explainability
Explore other notions than input level explanations -> in the latent space
Robust training:
Re-visit tighter approximation for training?
Applications beyond robustness and explainability: contrastive learning, robust segmentation…
Ever-going problem of efficiency
Ever-going problem of efficiency
Ever-going problem of efficiency

## Slide 52: Future Work and important challenges
Robust training
Re-visit tighter approximation for training?
Applications beyond robustness and explainability: contrastive learning, robust segmentation…
Verification
Automated input partitioning (beyond bissection)
Verification of more complex architectures
Verification of more complex properties
Explainability
True end to end learning of which input are relevant jointly with the robust training for explainability
Explore other notions than input level explanations -> in the latent space
Ever-going problem of efficiency
Ever-going problem of efficiency
Ever-going problem of efficiency
Robustness Verification for Transformers [Shi 2020]
Verifying Global Neural Network Specifications using Hyperproperties [Boetius 2023]
On the Paradox of Certified Training [Jovanović 2021], Gaussian Loss Smoothing Enables Certified Training with Tight Convex Relaxations [Balauca 2024]
Formal Abductive Latent Explanations for Prototype-Based Networks [Soria 2026]

## Slide 53: If you must only remember one thing
Over-approximations: versatile tool that can be leveraged in multiple ways to bring trust to AI systems
Trust should be an integral part of the design / training choices!
Questions ?

## Slide 54: Additional content
4

## Slide 55: LIBRA (Fairness)
 |  | Coverage (%) |  | Execution Time (s) | 
L | U | Width | ReCIPH | Width | ReCIPH
1 | 2 | 68.8% | 87.5 % | 0.26 | 0.11
 | 6 | 68.8% | 87.5 % | 0.51 | 0.20
4 | 2 | 100 % | 100 % | 2.60 | 2.10
 | 6 | 100 % | 100 % | 2.65 | 2.10
LIBRA https://caterinaurban.github.io/project/libra/
Notes: Tool for Fairness Certification of Neural Networks
First step: input partitioning and forward analysis using abstract domains (i.e. linear approximations)
On sub-problems where # instable ReLU is low enough: complete backward analysis to certify fairness
End-result: fairness coverage of entire input space

## Slide 56: VNN Comp 2024
Benchmark | PyRAT Rank | Notes
cGAN | 1 / 6 | First rank position are shared with at least one other tool. Global ranking was 2 out of 8 submitted tools
LinearizeNN | 1 / 4 | 
Collins RUL CNN | 5 / 7 | 
TLL Verify Bench | 1 / 8 | 
ACAS Xu | 3 / 8 | 
Dist Shift | 1 / 5 | 
PyRAT with ReCIPH input partitioning is used for 6 out of 12 benchmarks
VNN Comp 2024 report https://arxiv.org/abs/2412.19985
Verification is still a hard challenge!
Notes: Transition :
Verification remains a very active field. Standardly trained network are very challenging to verify.
Orthogonally to verifying network post-training, there is an area of research dedicated to inducing robustness during training.

## Slide 57: Local Linearity and Catastrophic Overfitting

## Slide 58
Source of approximations: handling of the non-linearities (activation functions)
Parallel: WK [Wong2017], FastLin [Weng2018], Neurify [Wang2018], DeepZ [Singh2019], CROWN [Zhang 2018], DeepPoly [Singh 2019]
(Non-exhaustive list)

## Slide 59: Supervised Training (Classification)
(Logits)
Panda
Not Panda
Estimation of the error of the model (using a surrogate loss function)
Gradient Descent: Update of the parameters in the opposite direction of the gradient to minimize the error. Stochastic Gradient Descent (SGD): compute the gradients and do the update over small batch of inputs randomly drawn from the dataset. One epoch = one full pass over the dataset
Goal: empirical risk minimization. Expectation of the loss function over the dataset

## Slide 60: Supervised Training (Classification)
Panda
Not Panda
Estimation of the error of the model (using a surrogate loss function)
Update of the parameters to minimize the error

## Slide 61: Robust Learning, more formally
[Madry 2018] Goal of robust training:
= typically the cross-entropy
Adversarial training: under-approximate solution of inner-maximization using some attack algorithm
Certified training: over-approximate solution using differentiable bounding algorithm (in practice IBP)
  with and the output bounds computed with IBP
  with an adversarial perturbation

## Slide 63: Interval Bound Propagation

## Slide 64: Expressive Losses
Expressive Losses for Verified Robustness via Convex Combinations [De Palma 2024]
Different ways of combining have been proposed:
MTL-IBP
CC-IBP
Exp-IBP

## Slide 65: Expressive Losses

## Slide 66: Trade Offs of CT + AT in CO setting

## Slide 67: Sensitivity of CT + AT to

## Slide 68: Time trade offs

## Slide 69: Prevent CO in Softplus networks

## Slide 70: Limits
CIFAR-100
CIFAR SVHN
On CIFAR-100: CO is mitigated, but high cost in empirical robustness (tuning adapted to the epsilon could help)
On SVHN: MTL-IBP fails. MTL-IBP tuning is very sensitive compared to Exp-IBP, especially for deep networks.

## Slide 71: Comparisons with ELLE

## Slide 72: Comparisons with ELLE

## Slide 73: Some clean accuracies
CIFAR-10, CNN-7, 160 epochs

## Slide 74: Low Epsilon on standard network?

## Slide 75: ReCIPH as traversal order

## Slide 76: Qualitative Results
FS+CT+AT
CT + AT
AT

## Slide 77: Robustness and XAI 1

## Slide 78: Robustness and XAI 2

## Slide 79: Robustness and XAI 2

## Slide 80: Robustness and XAI 3